## Slide 1
Cfe Higher Physics
Unit 3.2
Resistors in Circuits

## Slide 2
3.2.1 Introduction
Current, I, measured in Amperes, is a flow of charged particles.
Electrons are negatively charged and so flow from the negative side of a power supply to the positive side.
To measure the current through a component place an ammeter in series with it.
An ammeter should have a very low resistance.
Charge, Q, measured in coulombs (C) is transferred when electrons flow.

## Slide 3
Voltage or potential difference, V, measured in volts (V), is the number of joules of energy gained or lost by 1 coulomb of charge moving between two points.
(If one of these points is earthed, the voltage is called a potential).
The bigger the potential difference, the bigger the current.
To measure the potential difference across a component, place a voltmeter in parallel with it.
A voltmeter should have a very high resistance
Resistance, R, measured in ohms (), tells us how difficult it is for the current to get through.
The bigger the resistance, the smaller the current.

## Slide 4
(a) Series Circuits
In series the components are joined end-to-end, one after the other.
There is only one path for the current to flow in a series circuit.
V2
V1
A1
A2
Vs
Vs = supply voltage
Current is the same at all points  A1 = A2
The supply voltage is equal to the sum of the voltages across the components  Vs = V1 + V2
Note
V  R i.e. the biggest resistor takes the biggest share of the voltage.
So if R1 = R2 then V1 = V2, If R1 = 2R2 then V1 = 2V2

## Slide 5
e.g.
2V
1V
3 V
10 
5 
As each coulomb of charge has to pass through both resistors it loses energy in both resistors, so the voltage divides.
The total resistance of the circuit is equal to the sum of the individual resistances
 RT = R1 + R2 ……………….. (RT = equivalent series resistance)
N.B. RT is always greater than the largest resistor present.
e.g. 1  and 1000  in series; RT = 1 + 1000 = 1001  ( >1000 )

## Slide 6
(b) Parallel Circuits
A1
V2
V1
Vs
A3
A2
R1
R2
The circuit current is equal to the sum of the currents in the branches
 A1 = A2 + A3
V across components in parallel is the same  Vs = V1 = V2
Note I  1/R i.e. the biggest resistor has the smallest current flowing through it.
So if R1 = R2 then A2 = A3, If R1 = 2R2 then A2 = ½ A3

## Slide 7
6A
20V
20V
20V
4A
2A
10Ω
5Ω
e.g.
As each coulomb of charge can only pass through one resistor, it gives up all its available energy in that resistor, so the potential difference across each resistor is the same.
Check:
V10Ω = IR = 2 x 10 = 20V
V5Ω = IR = 4 x 5 = 20V

## Slide 8
Combinations of Resistors

## Slide 9
3.2.3 Combinations of Resistors
(A) Resistors in Series
vS
R1
R2
R3
I
From conservation of energy applied to resistors in series:
VS = I R1 + I R2 + I R3
I RT = I R1 + I R2 + I R3 (RS = equivalent series resistance)
RT = R1 + R2 + R3
Since the current in the same everywhere.

## Slide 10
(B) Resistors in Parallel
R1
R2
R3
I
I1
I2
I3
V
From conservation of charge i.e. the total charge per second (current) passing through R1, R2 and R3 must equal the charge per second (current) supplied from the cell.
I = I1 + I2 + I3
(RT = equivalent parallel resistance)
Since the voltage across each resistor is V.
Unit of resistance: ohm (), scalar. (1  = 1 volt per amp, 1  = 1 V A–1).

## Slide 11
The total resistance of the circuit is found using
1 1
RT R1 R2
=
+
+ …....
RT = equivalent parallel resistance
N.B. RT is always less than the smallest resistor present
e.g. 1 Ω and 1000 Ω in parallel;
1 1
RP 1 1000
=
+
1000 1
RP 1000 1000
=
+
=
1001
1000
RP
=
1000
1001
= 0.99 Ω (i.e. < 1Ω)

## Slide 12
N.B. If the resistors in parallel are all identical, it is quicker to divide the value of one resistor by the number of resistors present to get the correct RT.
e.g. four 8Ω resistors in parallel:
RP = 8/4 = 2Ω
1/RP = 1/8 + 1/8 + 1/8 + 1/8 = 4/8
RP = 8/4 = 2Ω

## Slide 13
(c) Mixed Circuits
Calculate the resistance between X and Y.
10Ω
10Ω
10Ω
10Ω
10Ω
X
Y
Re-draw the circuit
20Ω
10Ω
20Ω
X
Y

1 1 1
RP R1 R2 R3
=
+
+

1 1 1
RP 20 10 20
=
+
+

1 + 2 + 1 4
RP 20 20
=
=

20
4
=
RP
=
5Ω

## Slide 14
(d) Calculating Voltage (Current)
Ohm’s Law V = I R
 Current drawn from supply =
Total voltage supplied
Total resistance
OR Current through a component(s) =
Voltage across component(s)
Resistance of component(s)

## Slide 15
Example 1 (the potential divider) page 5
Remember when voltage divides, the biggest resistor will always take the biggest share of the voltage.
Calculate the p.d. across the 12Ω resistor.
V1
V2
R1= 24 Ω
R2= 12 Ω
Step 1: Calculate the total resistance.
Total resistance, RT =
24 + 12 = 36Ω

## Slide 16
Step 2: Calculate the current through the resistors.
The resistors are in series so the current through each is the same.
If we use 12 V, the total voltage, we have to use the total resistance.
Current, I =
V
R
12
36
=
Step 3: Calculate the p.d. across the 12  resistor using Ohm’s Law.
V = I R
12
36
=
X 12
= 4V
The values of V1 and V2 depend on R1 and R2. Check that
for a voltage divider:
V1 R1
V2 R2
=
24
4 12
=
 2 = 2

## Slide 17
Example 2 (the potential divider with a parallel section)
page 6
Calculate the p.d. across AB.
5V
1.7 kΩ
2.2 kΩ
1.0 kΩ
A
B
Step 1: Find resistance of parallel section (RP)

1 1
RP R1 R2
=
+

1 1
RP 2.2 1.0
=
+

2.2+1.0
RP (2.2x1.0)
=

3.2
RP 2.2
=

2.2
3.2
=
RP
 RP = 0.6875

## Slide 18
Now find RT :
RT = 1.7 + 0.6875 = 2.3875 kΩ
Step 2: Find I in circuit
I =
V
R
=
5
2.3875k
Step 3: Find p.d. across AB
VAB = IAB x RAB But we do not have IAB,
we have total I through the parallel branches.
 VAB = VP = IPRP
 VP
=
5
2.3875k
x 0.6875k
 VP = 1.4 V = VAB
(V2.2kΩ = 1.4V!)

## Slide 19
Example 3 page 7
A
36 V
+
-
Rx
Ry
12 V, 3A
2
(a) What is the reading on the ammeter?
3A
(b) Calculate the resistance of Ry when the lamp is operating correctly.
Ry =
Vy
I
 need Vy first!

## Slide 20
36 = Vx + Vy + 12
36 = IR + Vy + 12
36 = (3x2) + Vy + 12
36 = 18 + Vy
Vy = 36 -18 = 18V
Ry =
Vy
I
Now use
Ry =
18
3
Ry = 6

## Slide 21
Example 4 page 8
A potential divider is used to provide an output voltage VO from a 10V supply as shown.
VO
10V
X
Y
1.2 k
The resistance of resistor X is 12 k and the output voltage
required is 60 V.
Calculate the resistance of resistor Y.
Step 1: Find I
I =
VX
RX
I =
10-6
1200
I =
4
1200
Step 2: Find R
Ry =
Vy
I
Ry =
6
(4/1200)
Ry = 1800 = 1.8k

## Slide 22
10V
X
Y
Z
1.2 k
(b) A load resistor Z is now connected across the output as shown.
Load resistor = a resistor across
which a voltage is required.
Explain why the voltage across Z is less than 60 V.
When Z is placed in parallel with Y, the combined resistance of Y and Z is less than Y alone.
Vout  R, so if R has decreased when Z is added, Vout must decrease.

## Slide 23
(c) Calculate the voltage across resistor Z when its resistance is 47 k.
1 1
RP 1.8 4.7
=
+
=
4.7 + 1.8
1.8 x 4.7
=
6.5
8.46
 RP
=
8.46
6.5
= 1.3kΩ
 RT = 1.3k + 1.2k = 2.5kΩ
I =
V
R
10
2500
=
 VYZ = IP RYZ
10
2500
=
x 1300
= 5.2V

## Slide 24
The following examples have proved very difficult for Higher pupils to solve.
Example 5 Page 9
Calculate the potential difference (p.d.) across AB
18 Ω
6 Ω
30 Ω
15 Ω
3V
9V
A
B
N.B. The top branch of the circuit has NO affect on the bottom branch and vice versa. They are independent of each other.
RT = 6 + 18 = 24Ω
I =
V
R
9-3
24
=
6
24
=
VAB = I RAB
6
24
=
x 6
VAB = 1.5V

## Slide 25
Example 6 Page 10
A battery of e.m.f. of 120 V and negligible internal resistance is connected as shown in the circuit opposite.
(a) Calculate the p.d. across the 5 k resistor.
RT = 3k + 5k = 8kΩ
I =
V
R
12
8000
=
V5k = I R
12
8000
=
x 5000
= 7.5 V

## Slide 26
(b) Two further resistors and a variable resistor are added to the circuit as shown.
Show by calculation that there is no current in the 10 k resistor.
If there is no current in the 10kΩ resistor then the p.d. across it is 0V, i.e. potential at X = potential at Y
X
Potential at X = p.d. across R2
= 7.5 V (see (a))
Y
RT = 22.5k + 37.5k = 60kΩ
I =
V
R
12
60k
=
VY = p.d. across R4
12
60k
=
x 37.5k
= 7.5 V
p.d. between X and Y
= 7.5 – 7.5 = 0V

## Slide 27: Wheatstone Bridges

## Slide 28
3.2.4 Wheatstone Bridge Circuit
A Wheatstone bridge has four resistors arranged in two parallel branches, each of two resistors.
The Wheatstone bridge is used
(i) to find the values of unknown resistors.
A voltmeter is connected between the mid points of the pairs of resistors in each branch.
When the reading on the voltmeter is 0 volts, there is no potential difference between X and Y and the bridge is said to be balanced.
V
R1
R3
R2
R4
X
Y

## Slide 29
(ii) or as an input circuit in electronics.
2000 Ω
4000 Ω
4000 Ω
R
V2
+ V
0 V
V1

## Slide 30
A
C
V
12V
R1 = 8Ω
R3 = 4Ω
R2 = 4Ω
R4 = 2Ω
X
Y
B
D
0V
-
+
The Balanced Wheatstone Bridge
Consider the following circuit with four resistors R1, R2, R3 and R4.
Current from the battery will flow through the two branches of the circuit.
The resistance of the current path AXB is 12  therefore the current in this path is 12/12 = 1 A.
The p.d. across the 8  resistor is 1  8 = 8 V, therefore the potential of point X is +8 V.
The resistance of the current path CYD is 6  therefore the current in this path is 12/6 = 2 A.
The p.d. across the 4  resistor is 2  4 = 8 V, therefore the potential of point Y is +8 V.

## Slide 31
When the circuit is balanced the voltmeter reading reads zero
i.e. the potential difference between X and Y is zero.
There is therefore no potential difference between points X and Y and the voltmeter reading is zero.
The bridge is then said to be balanced.

## Slide 32
Relationship among the resistors in a balanced Wheatstone bridge
When the bridge is balanced, VAX = VCY and VXB = VYD
so, I1R1 = I2R2 and I1R3 = I2R4
Dividing these equations,
or,
Is described as the balanced condition.

## Slide 33
Note:
1. The labels for the resistors i.e. 1, 2, 3, 4 only apply to this set up. In general it is the position in the circuit which is important.
2. To calculate the value of an unknown resistor two of the resistors e.g. R3 and R4 are known, R2 is a calibrated variable resistor which can be changed until the circuit is balanced. The value of R1 may then be calculated.
3. A galvanometer is a sensitive meter that can be used in place of a voltmeter. A galvanometer can only handle very low potential differences.
A resistor is connected in
series to the galvanometer
to prevent damage to the
meter when the bridge is far
out of balance.
Switch S is used to short circuit R
when near balance to give greater
sensitivity.
G
X
R
Y
S

## Slide 34
Example 1 Page 32
If the bridge is balanced, calculate the value of resistor S.
P = 1 k Q = 2 k R = 3 k
V
P
Q
R
S
R1
R2
R3
R4
=
P
R
Q
S
=
1k
3k
2k
S
=
S =
3k x 2k
1k
= 6 k Ω

## Slide 35
(b) After a period of use the potential difference across the battery in the circuit decreases to half its original value. What effect does this have on the voltmeter reading?
None. The bridge is still balanced

## Slide 36
B. The Out Of Balance Wheatstone Bridge.
The graph below shows the variation of potential difference between X and Y as one of the resistors is changed by small amounts from its value when the bridge is balanced.
0
ΔR
ΔV

## Slide 37
Conclusion:
The out of balance p.d. is directly proportional to the change in resistance.
i.e. V  R (if R is small).
This linear variation of potential difference with change in resistance is used in electronics
e.g. if one of the resistors is replaced by a heat sensitive resistor (thermistor) then the out of balance voltmeter reading indicates temperature change.

## Slide 38
Example 2 Page 33
Describe how the out of balance voltage in a Wheatstone bridge circuit can be used to measure temperature.
V
R1
R2
R3
R4
Melting ice

## Slide 39
R4 is a thermistor which is placed in melting ice. R1, R2 and R3 are adjusted until the bridge is balanced i.e. V = 0.
R4 is now placed in boiling water and the reading on the voltmeter is noted.
A calibration graph can now be drawn.
0
T (°C)
V +
V -
100
Any temperature can now be estimated from the graph.
(In drawing the graph we have assumed that the relationship between the out of balance voltage and temperature are linear i.e. forms a straight line.)

## Slide 40
Example 3 Page 34
A Wheatstone bridge circuit is shown below.
V
12.0 V
X
Y
R2
R4
R3
R1
22.5kΩ
5kΩ
3kΩ
(a) Show that the bridge is balanced when the variable resistor R4 is set to 375 kΩ.
R1
R2
R3
R4
=
3k
5k
22.5k
R4
=
R4 =
5k x 22.5k
3k
= 37.5 kΩ

## Slide 41
(b) The variable resistor R4 is now set to 372 k and the p.d. between the points X and Y is measured.
The resistance of R4 is then altered to the values shown in the table below.
Complete the table to show the voltmeter readings, including sign, that would be obtained for each of the remaining resistance values.
Resistance of R4/kΩ | Voltmeter reading/mV
37.2 | -22.5
37.3 | 
37.4 | 
37.5 | 
37.6 | 
- 15
- 7.5
0
+ 7.5

## Slide 46: E.M.F and Internal Resistance

## Slide 47: What we will cover today:
Concept of electromotive force as the energy supplied to every coulomb of charge leaving the source.
Link between the E.M.F and the T.P.D as the actual supply voltage.
Determine Ir using a graph

## Slide 48
3.2.5 E.M.F.
A source of electrical potential energy, such as a battery, provides an electromotive force (e.m.f.) to drive an electron current through the circuit.
The units of e.m.f. are the same as those of p.d. i.e. the volt (joule per coulomb), scalar.
The electromotive force (e.m.f.), E, of the source, is the electrical potential energy supplied to each coulomb of charge which passes through the source.

## Slide 49
Experiment 1
A
V
The voltmeter is measuring the voltage across the terminals of the source (and this is the same as the voltage across the bulb).
This voltage is called the terminal potential difference (t.p.d.) and is the number of joules per coulomb that the battery supplies to the bulb.
i.e. the number of joules per coulomb that you can put to good use.

## Slide 50
Experiment 1
A
V
Set up the circuit as shown and record the voltage across the supply with the switch open. This is the e.m.f. of the source.
With the switch closed record a value of the current and the new voltage.
Why do you think there is a difference in the voltages?.
What would happen he current and voltage values if you added more bulbs in parallel?.

## Slide 51
Experiment 1.5
A
V
Number of lamps lit | Current (A) | TPD (V) | Lost Volts (V)
1 |  |  | 
2 |  |  | 
3 |  |  | 
Continue to add branches to the circuit and calculate the volts that are lost from your initial measurement.

## Slide 52
A
V
E
r

## Slide 53
Calculate the internal resistance of the battery for each data set. Use the current measured and the lost volts in the following equation.

## Slide 54
Energy and Power

## Slide 55
3.2.2 Energy and Power
Ew = QV, but Q = It 
P = I V, but V = I x R 
 
P = I V
P = I V, but 
P = I  I R 
P =  V 

## Slide 56
Experiment 2
Circuit :
R
A
V
The voltmeter is measuring the voltage across the terminals of the source (and this is the same as the voltage across R).
This voltage is called the terminal potential difference (t.p.d.) and is the number of joules per coulomb that the battery supplies to the load resistance R
i.e. the number of joules per coulomb that you can put to good use.

## Slide 57
Procedure:
Set R to maximum resistance. Decrease R in steps, noting the current and voltage readings each time.
Draw a graph of voltage against current.
Results:
0
I
V (t.p.d.)

## Slide 58
Conclusions:
The terminal potential difference, Vt.p.d., is not constant.
As current increases, Vt.p.d. decreases.
This is because the cell has an internal resistance that is given the symbol r.
Energy is lost in driving the current through the chemicals that make up the cell.
As the current increases, more of the available energy is "lost" inside the cell – the cell gets warmer and there is therefore less energy available to put to good use across R.
The terminal potential difference Vt.p.d. = E when no current is flowing
i.e. on open circuit. When no current is taken from the power supply,
no energy is wasted.
When a current does flow, the terminal potential difference is always
less than the e.m.f.
The difference between E and Vt.p.d. due to the energy lost inside the cell because of its internal resistance is termed the lost volts.
Lost volts = E – Vt.p.d..

## Slide 59
New representation of circuit:
Any power supply can be thought of as a source of constant e.m.f. in series with a small resistance (the internal resistance).
A
V
E
r
R

## Slide 60
Which is equivalent to
R
E
r
V divides across r and R
E = Vr + VR
E = Ir + IR
If R ↓, I ↑ , Ir ↑ and I R ↓
If R halves, I does NOT double!

## Slide 61
By conservation of energy, the energy per coulomb converted by the battery must equal the sum of the energies per coulomb converted in r and R.
 E = p.d. across r + p.d. across R (since voltage divides in series)
 E = Ir + IR (since V = I R)
The potential difference across the external resistor, IR, is the same as the t.p.d. (assuming the ammeter has no resistance) i.e. IR = Vt.p.d.
 E = Ir + Vt.p.d.

## Slide 62
Internal resistance
External (load) resistance

## Slide 63
The following formulae are useful:
To calculate the current drawn from a cell, rearrange E = Ir + IR
= I (R +r)
( I = V/R )
To short circuit the cell, R is set to 0 .
short circuit (maximum) current

## Slide 64
We need to look at the equation, , in more detail:
As I increases, Ir increases and so Vt.p.d. decreases (assuming E = constant.)
Ir is called the “lost volts” – it heats up the cell.
N.B. If I = 0 then Ir = 0 
 Vt.p.d. = E on open circuit (when no current flows)

## Slide 65
(b)

c.f. y = mx + c
 y  Vt.p.d., m  (- r), x  I, c  E
Y intercept (c) = E
Gradient (m) = ( -r)
=
y2 – y1
x2 – x1
Short circuit current (the max current that can be drawn from the cell)
Vt.p.d.
I
0

## Slide 66
Example 1 Page 23
A car battery is connected in a circuit as shown to study how the voltage across the battery varies with the current drawn from it.
For each setting of the variable resistor R, switch S is closed momentarily and the voltmeter and ammeter readings are
recorded.
A graph of the results is shown opposite.
(a) Explain why the reading on the voltmeter decreases as the ammeter reading increases
(b) Use information from the graph to find:
(i) the e.m.f. of the battery;
(ii) the internal resistance of the battery;
(iii) the current from the battery if it is short circuited.

## Slide 67
(a) Explain why the reading on the voltmeter decreases as the ammeter reading increases
Voltmeter is measuring t.p.d.
Vtpd = E – Ir SO if I increases then Ir increases
and since E = constant Vtpd must decrease.
(b) Use information from the graph to find:
(i) the e.m.f. of the battery;
(ii) the internal resistance of the battery;
(iii) the current from the battery if it is short circuited.
(i) E = Vtpd when I = 0 i.e. intersection of Y-axis = 12V

## Slide 68
(ii) r = -m, (x1, y1) = (0,12) (x2,y2) = (80,8)
m =
y2 – y1
x2 – x1
8 – 12
80 – 0
=
= -0.05
r = -m = 0.05Ω
(iii) Short circuit I = largest I = intersection of x-axis = 240V
OR I = E/r = 12/0.05 = 240A

## Slide 69
A signal generator can be considered as a source of e.m.f. with an internal resistance.
When testing loudspeakers, a signal generator with an internal resistance of 16  is set to produce an e.m.f. of 24 V.
Example 2
32 Ω
(a) Find the current in the loudspeaker
(b) Calculate the voltage across the loudspeaker.
(c) Calculate the power delivered to the loudspeaker.
(d) Calculate the energy 'lost' inside the signal generator every second

## Slide 70
(a) Find the current in the loudspeaker
I =
Total voltage supplied
Total resistance
=
E
r + R
=
24
(16 + 32)
= 0.5 A
(b) Calculate the voltage across the loudspeaker.
Vtpd = I R
= 0.5 x 32
= 16V
OR Vtpd = E – Ir
= 24 – (0.5 x 16)
= 16V

## Slide 71
(c) Calculate the power delivered to the loudspeaker.
P = I Vtpd
= 0.5 x 16
= 8.0 W
OR P = I2R
= 0.52 x 32
= 8.0 W
(d) Calculate the energy 'lost' inside the signal generator every second
W = I t V where V = lost volts = V across r = Ir
W = It x Ir = 0.5 x 1 x 0.5 x 16
W = 4.0 J

## Slide 72
Example 3
The circuit shown includes a cell with an e.m.f. of 160 V and internal resistance r.
The following readings are taken from the meters;
reading on the ammeter = 004 A
reading on the voltmeter V1 = 120 V
reading on the voltmeter V2 = 030 V
(a) Calculate the value of the lost volts in the circuit.
(b) Calculate the internal resistance, r, of the cell.
(c) The resistance of the variable resistor is altered so that the reading on the ammeter is 002 A.
What is the resistance of the variable resistor now?
(d) The resistance, R, of the variable resistor is now decreased. What effect has this on the terminal potential difference, Vt.p.d. of the cell?

## Slide 73
(a) Calculate the value of the lost volts in the circuit.
(b) Calculate the internal resistance, r, of the cell.
Vtpd = V1 + V2 = 1.20 + 0.30 = 1.50V
Lost volts = E – Vtpd = 1.60 – 1.50 = 0.10V
Lost volts = Ir
r =
Lost volts
I
=
0.10
0.04
= 2.5 Ω

## Slide 74
(c) The resistance of the variable resistor is altered so that the reading on the ammeter is 002 A.
What is the resistance of the variable resistor now?
I =
E
r + R

0.02 =
1.60
2.5 + R

0.02 (2.5 + R) = 1.60

(0.02 x 2.5) + 0.02 R = 1.60

0.02 R = 1.60 – 0.05

R =
1.55
0.02
= 77.5

Variable R = 77.5 – 30 = 47.5Ω

## Slide 75
(d) The resistance, R, of the variable resistor is now decreased. What effect has this on the terminal potential difference, Vt.p.d. of the cell?
Vtpd = E - Ir
 If R decreases then I increases
 Ir increases ( E = constant)
 Vtpd decreases

## Slide 76
Example 4 Page 26
A second 40  resistor is connected in parallel with the first.
What is the new current and the new t.p.d.?
4.0 Ω
E = 1.5 V
I = 0.30 A

## Slide 77
Need r first :
I =
E
r + R
0.3 =
1.5
r + 4
0.3 (r + 4) = 1.5
0.3r + 1.2 = 1.5
0.3r = 1.5 – 1.2 = 0.3
r =
0.3
0.3
= 1Ω
New
I =
E
r + R
I =
1.5
1 + RP
RP = 4/2
= 2Ω
I =
1.5
1 + 2
= 0.5A
New Vtpd = I R
= 0.5 x 2
= 1.0 V

## Slide 78: Cells in Series and Parallel

## Slide 79
3.2.6 Cells in Series and Parallel
If cells are placed in series, the total e.m.f. is the sum of the individual e.m.f.’s providing the polarity of the connections is taken into account.
Example 1 Page 27
Six identical cells each of e.m.f. 2 V and internal resistance 05  are connected in series.
(a) What is the overall e.m.f. and internal resistance?
2V
2V
0.5 Ω
0.5 Ω
E = 2 x 6 = 12V
r = 0.5 x 6 = 3Ω
Each coulomb of charge passes through every cell.
(b) What is the short circuit current?
I = E/r = 12/3 = 4A

## Slide 80
Example 2 Page 27
Four identical cells each of e.m.f. 3 V and internal resistance 1  are connected in parallel.
(a) What is the overall e.m.f. and internal resistance?
E = 3V
rp = ¼ = 0.25Ω
Each coulomb of charge can only pass through 1 cell.
(b) What is the short circuit current?
I = E / r = 3 / 0.25 = 12A

## Slide 81
Example 3 Page 28
4.0 Ω
1.0 Ω
1.0 Ω
5.0 Ω
1.2 Ω
2.0 V
4.0 V
N.B. cells are wrong way round, E = 4 – 2 = 2V
Find:
(a) current in the 50  resistor.
I =
E
r + R
I =
2
1+5+1.2+0.8
1/RP = ¼ + 1/1 = (4+1)/4 = 5/4
RP = 4/5 = 0.8Ω
I = 0.25A

## Slide 82
(b) the p.d. across the 10  external resistor
VP = IP RP
V = 0.25 x 0.8
V = 0.2V
(c) t.p.d. of 40 V cell
Vtpd = E - Ir
Vtpd = 4 – (0.25 x 1.2)
Vtpd = 3.7V