## Slide 1: S3/S4 Physics
Potential Dividers

## Slide 2: Potential Dividers
A potential (voltage) divider circuit is a very useful circuit.
A potential (voltage) divider circuit usually consists of a supply voltage and resistive components (usually two) connected in series.
The supply potential (voltage) is divided up across the resistors in the circuit.

## Slide 3: Potential Dividers
V1
Vs
V2

## Slide 4: Potential Dividers
For all potential (voltage) dividers the following is true:
The larger resistance will always have the greater potential difference (voltage ) across it
The sum of the individual potential differences (voltages) will be equal to the supply voltage
V1 + V2 = Vs

## Slide 5: Potential Dividers
The ratio of the potential differences (voltages) will depend on the ratio of resistance values.
This can also be written as:
V1 / V2 = R1 / R2

## Slide 6: Potential Dividers
V1 = ?
Vs
V2 = 16 V

## Slide 7: Potential Dividers
Example One
In the previous circuit R1 = 20 Ω and R2 = 80 Ω. Calculate the value of V1.
V1 / V2 = R1 / R2
V1 / 16 = 20 / 80
V1 / 16 = 0.25
V1 = 0.25 x 16
V1 = 4 V

## Slide 8: Potential Dividers
V1 = 25 V
Vs
V2 = 10 V

## Slide 9: Potential Dividers
Example Two
In the previous circuit R2 = 80 Ω. Calculate the value of R1.
V1 = R1
V2 R2
25 = R1
10 80
R1 = 25 x 80
10
R1 = 200 Ω

## Slide 10: Potential Dividers
V1
Vs
V2

## Slide 11: Potential Dividers
For the previous circuit calculate the missing value in each row.
V1 (Volts) | V2 (Volts) | R1 (Ohms) | R2 (Ohms)
5 | 15 |  | 30
 | 30 | 40 | 60
5 | 2 |  | 8
 | 12 | 60 | 36
4 | 1 | 24 | 
35 |  | 14 | 6

## Slide 12: Potential Dividers
Answers
V1 (Volts) | V2 (Volts) | R1 (Ohms) | R2 (Ohms)
5 | 15 | 10 | 30
20 | 30 | 40 | 60
5 | 2 | 20 | 8
20 | 12 | 60 | 36
4 | 1 | 24 | 6
35 | 15 | 14 | 6

## Slide 13: Potential Dividers
Not all potential (voltage) divider circuits can be solved using ratios.
An alternative equation is shown below.

## Slide 14: Potential Dividers
V1
Vs
V2 = ?

## Slide 15: Potential Dividers
Example
The value of R1 in the previous circuit is 150 Ω, and R2 = 300 Ω. Calculate the value of V2.
Solution
It can be useful to find the value in the bracket first.
R2 / (R1 + R2) = 300 / (150 + 300) = 300 / 450 = 0.67
V2 = 0.67 x Vs
V2 = 0.67 x 12
V2 = 8 V

## Slide 16: Potential Dividers
V1
Vs
V2 = ?

## Slide 17: Potential Dividers
For the previous circuit calculate V2 for each row.
VS (Volts) | R1 (Ohms) | R2 (Ohms) | V2 (Volts)
5 | 10 | 10 | 
6 | 12 | 24 | 
21 | 40 | 200 | 
12 | 5 | 3 | 
8 | 28 | 4 | 
15 | 20 | 30 | 

## Slide 18: Potential Dividers
Answers
VS (Volts) | R1 (Ohms) | R2 (Ohms) | V2 (Volts)
5 | 10 | 10 | 2.5
6 | 12 | 24 | 4
21 | 40 | 200 | 17.5
12 | 5 | 3 | 4.5
8 | 28 | 4 | 1
15 | 20 | 30 | 9